## Slide 1
Basic Setting Out
& Land Surveying
An activity for Scouts

## Slide 2
Objectives
1. Introduce the concept of setting out and land surveying by creating a giant picture from known points from given coordinates and measuring those points.
2. Work with your group to learn how to use a GNSS Receiver and Robotic Total Station to a basic level.
3. Learn the importance of working accurately, as well as how to communicate well with your group.
Instructions
Equipment
GNSS RTK Kits
Robot Total Station
Tripod
GNSS & Detail Pole
Small cones
Input your groups given coordinates into the GNSS handset. Take turns at reading out the coordinates and using the handset. Double check as you go.
Navigate to each point, paying close attention to the directions the GNSS is giving you. Once you find a point, place a cone on top of it.
Once you have set out all your points, use the total station to measure the cones as a line between your points. Take turns in using the total station and taking the points with the detail pole.
Return to your group and have a look at the picture you have made on the total station. Is it familiar?

## Slide 3
Basic Setting Out
& Land Surveying
Points to Set Out
Group A
Point | Easting | Northing
A1 | 432291.882 | 265671.685
A2 | 432292.132 | 265674.974
A3 | 432293.844 | 265677.534
A4 | 432297.006 | 265678.501
A5 | 432300.586 | 265677.703
A6 | 432302.577 | 265675.624
A7 | 432304.205 | 265672.501
A8 | 432304.922 | 265669.070

## Slide 4
Basic Setting Out
& Land Surveying
Points to Set Out
Group B
Point | Easting | Northing
B1 | 432309.444 | 265669.117
B2 | 432308.172 | 265673.805
B3 | 432306.130 | 265678.832
B4 | 432306.558 | 265684.631
B5 | 432312.299 | 265690.184
B6 | 432318.040 | 265684.631
B7 | 432318.468 | 265678.832
B8 | 432316.426 | 265673.805
B9 | 432315.155 | 265669.117

## Slide 5
Basic Setting Out
& Land Surveying
Points to Set Out
Group C
Point | Easting | Northing
C1 | 432332.716 | 265671.78
C2 | 432332.466 | 265675.069
C3 | 432330.754 | 265677.629
C4 | 432327.592 | 265678.596
C5 | 432324.012 | 265677.799
C6 | 432322.021 | 265675.719
C7 | 432320.393 | 265672.597
C8 | 432319.676 | 265669.165

## Slide 6
Basic Setting Out
& Land Surveying
Points to Set Out
Group D
Point | Easting | Northing
D1 | 432307.730 | 265659.053
D2 | 432312.085 | 265654.313
D3 | 432316.441 | 265659.053
D4 | 432314.893 | 265663.405
D5 | 432309.278 | 265663.405
D6 | 432299.909 | 265666.159
D7 | 432312.409 | 265666.159
D8 | 432324.909 | 265666.159