## Slide 1
Basic Setting Out
& Land Surveying
Guide for Survey Companies

## Slide 2
Objective
The main objective of this activity is to introduce the practice of setting out and land surveying to young people in a fun way.
Use the latest survey equipment.
Complete a task, with an outcome which illustrates both survey disciplines.
Basic Setting Out
Equipment List
Robotic Total Station
RTK GNSS Kits
Tripod
Detail Pole
Enough Cones to
mark all the points
A sunny day !
Topics to discuss during the activity.
What do we set out in our profession.
Where have you seen the equipment out and about.
Other occupations related to surveying.
What other role does GNSS play in our day to day lives.
What are the types of things we measure for land surveying.
How does the equipment work.

## Slide 3
Basic Setting Out
Pre-Activity Instructions
Source an open area with ample space, approximately 50m x 50m
Find a rough co-ordinate of area and orientate your supplied DXF scout emblem in AutoCAD, to allow for co-ordinates to be produced, see below example.
Produce significant co-ordinates dependent on the size of the activity party and create a spreadsheet for each team, see below example.
Visit the proposed site to make sure your GPS drops in and it is suitable for use.
Activity Instructions
Set up the GNSS equipment, leader should set up the kit with the teams following – Highlight the cost of the equipment and the importance of looking after the kit!
Set-up the TS16, activity leader should do this for the group – Highlight the importance of a solid foundation with wide legs and at a height that is suitable for the user.
Create a job on the on the GNSS handset and input the co-ordinates from the supplied spreadsheets. – Highlight the importance of accuracy over speed, if it’s wrong now it will be wrong at the end! Ensure everyone inputs some co-ordinates.
Set out the points you installed on the total station, marking with a cone.
Orientate the TS16 – Complete while scouts are setting out.
Once all the cones have been laid out, make sure the GNSS kits are packed away – Importance of looking after the kit.
Get each scout to measure the location of their cone, leave the screen on map screen with the remaining scouts, the image will be drawn as the data is collected and the scouts can guess the image in real time.
Pack up the equipment.
Take a photo of the image and ask if anyone has any questions.

## Slide 4
Points to Set Out Group A
With the logo in place in your desired location, you can now add points to the image, which the young people will then set out.
In our example we have divided the logo into 4 areas and used 8/9 points per area. You can add as many or few points as you like.
You can then present the coordinates in a format of your choice for the young people to use.
We have chosen a table, showing the point number, easting and northing.

## Slide 5
After talking the young people through the activity, you can get them inputting the coordinates into the GNSS handset. Make sure they all have a go at this and that they doubles check the numbers at the end.
Next, take them outside to your chosen survey area and get them to set out the points, making sure they each get a go. Mark each point with a cone or a flag.

## Slide 6
Once all the points are set out, set up a total station. You can either do this for them or let them have a go, depending on how much time you have.
Get some of the young people to survey the points they have just staked, and other to operate the total station. This works best if you can create a line string so they can see the picture being drawn as they go.

## Slide 7
Finally, if you have access to a drone, take a photograph of what the scouts have produced from above. This will make a nice memento of the activity.